## Slide 1: Food processing discussion
Notes: Stock image of cloud formations

## Slide 2: Food processing sector overview
Main uses of energy in food processing, across all subsectors1:
  Process heating and drying (59%)
  Cooling and refrigeration (16%)
  Mechanical equipment (12%)
  Infrastructure (HVAC and lighting) (8%)
Energy intensive processes include “materials reception and preparation; size reduction, mixing and forming; separation techniques; product processing technologies; heat processing; concentration by heat; chilling and freezing; post-processing operations; and utility processes”2
Wang, 2014, https://link.springer.com/article/10.1007/s12053-014-9256-8?utm_source=getftr&utm_medium=getftr&utm_campaign=getftr_pilot
UK Industrial Decarbonisation & Energy Efficiency Roadmaps to 2050 – Food and Drink, 2015, https://assets.publishing.service.gov.uk/government/uploads/system/uploads/attachment_data/file/416672/Food_and_Drink_Report.pdf

## Slide 3: Food processing sector overview
Compton et al., 2018, https://www.sciencedirect.com/science/article/pii/S1466856418301917
US electricity and natural gas use in the food processing sector

## Slide 4: Food processing sector overview – IEA data

## Slide 5: Food processing sector overview – IEA data

## Slide 6: Food processing sector overview – IEA data
Notes: Pakistan and South Asia do have food processing data in Comtrade, so this is likely missing in IEA

## Slide 7: Food processing sector overview
Meyers et al., 2016, https://www.sciencedirect.com/science/article/pii/S0360544216303644
From energy audits for small and medium-sized food and beverage companies in Austria, France, Germany, Poland, Spain, UK

## Slide 8: Food processing sector overview
Energy-saving and decarbonization options:
  Energy efficiency measures, process optimization
  Electrification of heat (heat pumps and electric boilers)
  CHP/cogen
  Fuel switching to renewables – biomass, solar thermal, geothermal heat pumps
  Waste heat utilization
  Food waste reduction, demand-side measures
  (Note: CCS, hydrogen seem less likely to play a role for food processing)

## Slide 9: Questions
Where do we want to add in the energy coefficients and non-energy costs?
  At the level of regional corn (Mt)  Corn (Mkcal), with a nesting for level of processing
    Pros – more detailed representation, allows for evaluation of shifting food consumption and preferences
    Cons – data availability?
  At the level of crops feeding into FoodDemand_Staples and FoodDemand_NonStaples
    Pros – simpler to implement
    Cons – would this adequately represent the heterogeneity of the sector? Changes in types of food consumed would not be reflected in changes in energy use

## Slide 10: Questions
Where do we want to add in the energy coefficients and non-energy costs?
  At the level of regional corn (Mt)  Corn (Mkcal), with a nesting for level of processing
    Pros – more detailed representation, allows for evaluation of shifting food consumption and preferences
    Cons – data availability?
  At the level of crops feeding into FoodDemand_Staples and FoodDemand_NonStaples
    Pros – simpler to implement
    Cons – would this adequately represent the heterogeneity of the sector? Changes in types of food consumed would not be reflected in changes in energy use
Technologies
  Process heating and drying (including boilers) – biomass, coal, gas, refined liquids, (grid) electricity (inc. heat pumps), CHP, solar thermal, geothermal heat pumps
  Refrigeration and cooling – (grid) electricity (inc. heat pumps), CHP, geothermal heat pumps
  Mechanical equipment – (grid) electricity, CHP
  Infrastructure (HVAC + lighting) – (grid) electricity, CHP, gas (for space heating)

## Slide 11: Questions
Staples – processed
Heating – gas, electricity, etc
Cooling – electricity,
Other
Processed
Dairy – all fuels
Meat
Grain
Sugar
Fruits + veggies

## Slide 12: Brainstorming
Staples – processed
Heating – gas, electricity, etc
Cooling – electricity,
Other
Processed
Dairy – all fuels
Meat
Grain
Sugar
Fruits + veggies

## Slide 13: Brainstorming
Processed
Dairy
Meat
Grain
Sugar
Fruits + veggies
Each has a coefficient that can vary with time?
- Maybe there is a baseline level of energy use, then a multiplicative factor to represent level of processing? (where to derive)

## Slide 15: Food processing discussion
Notes: Stock image of cloud formations

## Slide 16: Structure possibilities
Food processing
Staples
Non-staples
More processed
Less processed
More processed
Less processed
Process heat
Electricity
Process heat
Electricity
Process heat
Electricity
Process heat
Electricity
Challenges:
How to disaggregate food production into more vs less processed in base years?
Separating energy used for staples vs non-staples
Advantages:
Can explicitly shift from less to more processed foods with time

## Slide 17: Structure possibilities
Food processing
Staples
Non-staples
Process heat
Electricity
Process heat
Electricity
Challenges:
Separating energy used for staples vs non-staples
Less explicit processing level (though this could still be indicated with changes in energy coefficients with time)
Advantages:
More straightforward to implement

## Slide 18: Structure possibilities
Food processing
Total food demand (staples + non-staples)
Process heat
Electricity
Biomass
Coal
Gas
Refined liquids
Electricity
CHP (heat)
Solar thermal
Geothermal heat pumps
Challenges:
Less explicit processing level (though this could still be indicated with changes in energy coefficients with time)
Advantages:
More straightforward to implement

## Slide 19: Structure possibilities
Food processing
Staples
Non-staples
Process heat
Electricity
Fruit/veg
Animal protein
All staples (rice, corn, wheat, other grain, root tuber)
Process heat
Electricity
Process heat
Electricity
Plant protein
Process heat
Electricity
Other*
Process heat
Electricity
Challenges:
Accurate calibration for all crops
Less explicit processing level (though this could still be indicated with changes in energy coefficients with time)
Advantages:
More explicit breakout of food types, matching their varied levels of processing required
*oil, fiber crops, sugar crops, misc.

## Slide 20: Potential strategies
Strategy 1:
  Use IEA data to directly calculate coefficients
    Challenge: disaggregating staples vs non-staples (or to finer categories)
Strategy 2:
  Obtain coefficients of energy use for processing for different products from literature estimates
    Challenge: high degree of variability in estimates, depending on location/sub-product type/etc.
    Possibility: obtain breakdown of heat vs electricity for each product to disaggregate process heat vs electricity
  Scale the theoretical coefficients so that the overall energy consumption matches IEA
    Challenge: IEA regions with zero energy used in food processing
    Assumption: relative level of processing is constant across crops in a given region

## Slide 21: Food processing energy intensity

## Slide 22: Food processing energy intensity and input crop intensity

## Slide 23: Food processing energy intensity and non-staples fraction

## Slide 24: Questions
Calibrate food processing to domestically produced crops, or domestically consumed crops (accounting for exports and imports)?
Use the same fuel ratios for each food product/staples vs non-staples?
  May be able to vary this based on literature